PROJECT    PROFILE

ON

POLYESTER NEEDLEPUNCHED GEO TEXTILES

July 2013

PREPARED BY

K’S TECHNICAL AND MANAGEMENT CONSULTANTS, VADODARA,

www.technicaltex.com, ph: +919825244940

FOR

OFFICE OF TEXTILE COMMISIONER, MINISTRY OF TEXTILES

INDEX

PAGE

PRODUCT AND ITS APPLICATIONS					2

AN OVERVIEW OF MARKET						3

SUGGESTED PROJECT SIZE						4

RAW MATERIALS:

AVAILABILITY, REQUIREMENT AND COST				5

TECHNOLOGY ASPECT							6

MANPOWERAND UTILITY: REQUIREMENT AND COST               7

INFRASTRUCTURE RQUIREMENT                                                 8

PROJECT COST AND MEANS OF FINANCE                                  9

FINANCIAL PROJECTIONS                                                            10

CRITICAL FACTORS / KEY ELEMENTS                                        11

RAW MATERIAL, PLANT AND MACHINERY SUPPLIERS           12

CHAPTER   I

Product   and its Applications

Geo textiles are used in Civil Engineering applications.  These are textile like flexible materials that aid in the construction work.

The primary function of Geo Textiles is to provide Separation between Subgrade and Soil, Filtration and prevention of fines from contaminating gravel layers and Reinforcing the soil strength.  There are several grades of Geo textiles and can be designed to meet the specific needs of each application.

Geo textiles can be made by Weaving Process, Nonwovens process or Knitting processes.  A majority of Geotextiles currently used is made from Nonwoven Processes.  The Nonwovens made by Needlepunching process is having special characteristics compared to those made by Spun bonding processes.  Needlepunch Nonwovens provide bulk and drainage properties whereas those made with spunbond have higher strength and modulus.

The product proposed in this project report is made a combination of Spunbond and Needlepunch process having a combination of properties suited for the various Geo textile end uses.  They are produced generally in widths upto 5 mtrs and weight range 90 to 500 gms per sq m.

Typical Geo textile end uses are

- Soil stabilization

- Soil Reinforcement

- Drainage

- Erosion Control

- Surface crack prevention in asphalt layer

Both Polypropylene and Polyester spunbond Nonwovens are used depending on the economics.  Polyesters generally provide higher strength for a given weight compared to Polypropylene.  The choice is purely economic decision and availability of material at a given time.

It appears,  in the long run that Polyester polymers will be cheaper than Polypropylene, hence increasingly polyester based geo textiles are coming into the market. Currently Indian market is served by Carded and Needlepunched Nonwovens manufactured using recycled polyester fibers.

CHAPTER II

An Overview of the Market

Geo-Textiles have very high market potential in India.  The recent study by the expert committee in Textile Commissioner’s office estimated a market size of

Rs. 1200 Crores in the coming years.

With increasing Government expenditure on Roads and other infrastructure projects like Dams, Railways, Port Connectivity projects etc., the requirement of Geo textiles for civil engineering can only go up.  One of the government report indicate that Rs 1,72,000 crores is earmarked for investment in Roads by National Highway Development Authorities.   This will be both Private Public Participation and mostly by BOT basis.  This would mean that completion of project in the quickest possible time is of prime importance.  Using Geo textiles the making of Highways can be speeded up, hence its use is imminent.  One of the lacunas of system in India has been specification of material and incorporation of the Geo textiles in the National Guidelines for Making Roads.  A beginning in this direction has been made by the Road Research Institute which has given guidelines for Geo textiles and Geo Synthetics in IRC-SP-59  section 701.  It will not be long before a clear guide line for use of Geotextiles will be issued by Road and Transport ministry of Government of India.

Government of Gujarat has is considering notification  that the roads with CBR (California Bearing Ration indicating the strength of soil in wet conditions)  of less than 3 should use Geo textiles to improve the soil stabilization.  In the coming years even City municipal authorities will consider use of Geo textiles to prevent pot hole formation and increase surface life in roads with heavy traffic.  Therefore the demand for suitable Geotextiles from both National Highway infrastructure building and local municipal corporation will come into effect soon.

Nonwoven Geotextiles is also used in making Geobags used in erosion control.  The recent incidence of high river bank erosions in Ganga, Bramhaputra and other major rivers has ensured a spate of new projects to control river bank erosion leading to substantial demand for Nonwoven material.

The Alternative use for Polyester spunbond is in products like, base material for Bituminous Roofing felt, Automotive Carpets and Rail track bed reinforcement. It has also found extensive use as Secondary Carpet Backing material in tufted carpets.

CHAPTER   III

Suggested Project Size and Location

The Geo textiles are used in roads in the width range 2.5 mtr to 4.5 mtrs depending on the type of road, embankment.  Generally a width of minimum 4.5 mtr is used  in Highways.  In some instances like Runways of the air port widths upto 5 mtrs are used.  However the practical constraint of transporting Geo textiles in rolls of width higher than 4.5 mtr makes this is the most convenient width for road application.

Due to high transport cost of sending Geo textiles form one corner of the country to other, it is likely that there will be more regional production of this material.

To cater to local demand (there by have competitive edge ) it is recommended that a minimum economic size of the project should be around 3000 tons per anum.

As Polyester polymer is competitively priced  and is predicted to be cheaper in the long run compared to Polypropylene, a machine capable of producing Geo textiles with Polyester Chips as raw material is chosen for this end use. With certain modification in plant and machinery recycled PET chips can also be used as raw material.

The technology chosen is  the latest, most efficient in terms of cost of conversion from Polyester chips to Nonwoven fabrics and is capable of producing a wide range of Geo-Textiles for  different end uses.  The Raw material available within the country can be easily used for manufacturing the products.

Key feature for such projects due to following features

- Local availability of Polyester chips  and waste PET chips of right grade

- Government regulation favoring use of Geo textiles in roads

- A large network of roads being built and reconditioned

- Good port facilities, if need for export arises

CHAPTER IV

Raw Materials:

Polyester Granules of Specification as below:

Intrinsic Viscosity			0.64  +/- .02

- COOH				< 30 M mol/10 ^6

Melting Point  			261 Deg C

TiO2					0.3-0.5

Water					,0.4%

Or Clean Recycled PET chips of IV- 0.7 to 0.8 of high purity can be mixed

CHAPTER   V

Technology Aspect

The process described below is the most economical in terms of investment per ton capacity and also  conversion cost per ton output.

# The process essentially consist of following steps

Polyester Chips Hopper (  Vibrating Screen ( Transport( Crystaliser  Drying(

# Screw Extruder( Melt Filter( spinning ( Airflow Drawing(tow spreader and

# web former( Pre Needlepunch( Winding

Polyester Chips of Filament grade are dried and extruded into filaments through several spinning beams.  The webs are drawn and spread to form a web and subsequently passed through a Pre-needling machine and Final needling machine to achieve the desired properties.

The process runs at a speed between 2 to 15 m per min depending on the weight per sq m of the product to be produced.  The average production capacity of the plant is 3000 tons per anum.

Typically the Input out put ratio is 1.05 : 1.00

- The machine can also produce felts for roofing felt applications.  The polyester spunbond substrate is suitable for manufacturing bituminous felts which are used for waterproofing

- The Polyester substrate produced on this machine can also be used for general filtration purposes after suitable finishing processes.

CHAPTER     V I

Manpower and Utility for 3 shift working

Manpower

Plant Manager			1

Shift Supervisors		7

Operators		     	33

Technicians			4

Marketing Manager		1

Accts/Admin			3

Sales				3

CEO				1

Total			          53

Utilities

Installed Power                       1000 KW

Transformer                            1200KVA

Actual running consumption  650KW

Water                                      2.5 cum /day

Compressed air                      50NM3 /min

CHAPTER   VII

Infrastructure   Requirements

Land				  3000 SQ M

Plant Building Requirements   60 mtr length x 15 mtr width x 6 mtr height

The Extruder and Drier region

is 24 mtr in height: 		 (area about 10 x 10 m )

Raw Material storage and

Finished goods storage:	  20 m x 15 m

Office	Building		  10 m x 10 m

Effluent:   			  NIL

CHAPTER    VIII

Project Cost and Means of Finance

| PARTICULARS | Rs. Lakhs |
| --- | --- |
| Land 3000 sq m x 500 per sq m | 15 |
| Building 1300 sq m x 8000/sq m( due to 24 m high in drier area) | 104 |
| Plant and Machinery incl. utilities- imported $2.5Million @Rs. 60/$ (Chinese Eqp) | 1500 |
| Piping , electrics and other assets | 80 |
| Margin for Working Capital | 250 |
| TOTAL | 1949 |

Means of Finance

| PARTICULARS | Rs. Lakhs |
| --- | --- |
| Capital | 585 |
| Term Loan | 1364 |
| TOTAL | 1949 |

CHAPTER     IX

FINANCIAL PROJECTIONS

| PARTICULARS | FIRST YEAR |
| --- | --- |
| PRODUCTION AT 60% CAP UTLISATION | 1800 TONS |
| PRODUCT- AVG | 300 GSM |
| SALES PRICE PER KG | RS. 150 |
| RAW MATERIAL PET CHIPS PER KG | Rs. 90 |
| CONVERSION COST FROM CHIP TO NEEDLEPUNCH FABRIC Rs./Kg (INCL 5% WASTE) | Rs. 25 |
| SELLING AND OTHER EXPENSES | RS. 12 |
| OPERATING MARGIN PER KG | Rs. 23 |
| OPERATING PROFIT | Rs. 414 |
| Return on Investment estimated | 20-25% |
| Payback period | 4 years approx. |

Current Sales price for the Product is Rs 150 PER KG for Geotextiles

Others products and applications get higher market prices.

CHAPTER X

Critical Factors   /  Key Elements

- Good quality  of PET CHIPS is highly essential for smooth running of plant.  Any let us in quality of chips will reduce plant capacity utilization and increase wastages.

- Lower Energy Costs is essential to remain competitive in business.

- Uninterrupted Power supply is essential as it is recognized as a  continuous process and generally cannot afford poor quality power also.

- As continuous run and capacity utilization are key to productivity, a regular order book is essential.

CHAPTER XI

Machine Suppliers

SHOYANG TEXTILE MACHINERY	:    CHINA

HONGDA                          		    	:    CHINA

NEUMAG                                          		:    GERMANY

MECCANICHE MODERNE              	:     ITALY

CHAPTER XII

Raw Material Suppliers

PET CHIPS

Reliance Industries	   		Mumbai

Ester India				Delhi

Futura  Organics		            Chennai

JBF				            Surat

JCT					Delhi